## Slide 1
CLASS 02 / SEP 1
NON-DESTRUCTIVE
MODELING
+ ASSIGNMENT 0.1 ISSUED TODAY
MODULE 0 / PROCEDURAL / ARC 3133
Notes: Two things today: make sure everyone can drive a graph, and issue 0.1. Most of the session is building — they should leave with a working operation tree.

## Slide 2
TUTORIAL 0.1 — THE LOGIC
Not the buttons. The four things a graph actually does.
01
A GRAPH IS A CHAIN OF OPERATIONS
Each node takes something in, does one thing, passes it on.
02
DATA FLOWS LEFT TO RIGHT
If a result is wrong, walk backwards until it stops being wrong.
03
GEOMETRY IS AN OUTPUT, NOT A THING
Nothing is 'made'. The graph describes how to make it, every time.
04
EVERY INPUT STAYS LIVE
Change a number at the start and everything downstream recomputes.
Notes: Ask before you explain: who got through it, who got stuck, where. Item 03 is the one that takes a while to sink in. Say it more than once.

## Slide 3
WHAT BROKE
Bring the file, not the description. Let's fix it live.
NOTHING APPEARS
Usually a preview toggled off, or a node not connected to output.
THE WRONG NUMBER OF THINGS
A list where a single item was expected, or the reverse.
IT WORKED, THEN STOPPED
Something upstream changed. Walk backwards node by node.
A NODE IS ORANGE / RED
It is telling you what it needs. Read the message before changing anything.
Notes: Fix at least two of these on the projector with a real student file. The habit you are teaching: read the error, then walk backwards. Not: delete and retry.

## Slide 4
WHY NON-DESTRUCTIVE
Same job both times: make the sphere bigger. Watch what it costs.
DESTRUCTIVE
CUBE
SPHERE
ONE MESH
gone
REBUILD FROM SCRATCH
The operations were discarded. The sphere no longer exists as anything you can edit.
NON-DESTRUCTIVE
CUBE
SPHERE
SUBTRACT
RESULT
CHANGE r HERE
EVERYTHING DOWNSTREAM
RECOMPUTES
Every input is still a live node. Edit it and the result rebuilds itself.
0.1 REQUIRES YOUR OPERATION HISTORY TO BE INTACT. I WILL ASK TO SEE IT.
Notes: Demo live: build it destructively, then try to enlarge the sphere. There is nothing to grab. Then the graph version — drag the radius and let them watch it update. The left panel is grey and struck through on purpose: those operations no longer exist. The right panel is a graph because that is literally what they are building.

## Slide 5
THREE BOOLEANS
Everything in Module 0 is built from these, applied in order.
UNION
A + B
DIFFERENCE
A − B
INTERSECTION
A ∩ B
Order matters. A − B is not B − A. Your instructions must make the order unambiguous.
Notes: Do A−B and B−A on screen back to back. Thirty seconds, and the point lands permanently. This is also the first place their written instructions will fail — 'subtract the cylinder' doesn't say from what.

## Slide 6
TRANSFORMATIONS ARE ARITHMETIC
Three operations on a coordinate. Nothing more mysterious than that.
MOVE
= ADD
THE MATH
x' = x + dx
y' = y + dy
z' = z + dz
(2, 1) + (3, 0) → (5, 1)
SCALE
= MULTIPLY
THE MATH
x' = x × f
y' = y × f
z' = z × f
(2, 1) × 2 → (4, 2)
ROTATE
= MIX x AND y
THE MATH
x' = x·cosθ − y·sinθ
y' = x·sinθ + y·cosθ
(1, 0) rot 90° → (0, 1)
Move and scale treat each coordinate on its own. Rotation is the only one where x and y have to talk to each other.
Notes: Point: none of this is new maths. They have been doing it since school — it just has geometry attached. The bottom line is the one worth dwelling on. Move and scale are per-coordinate, so they are easy. Rotation couples x and y, which is why it needs sine and cosine and why rotating about the wrong point is the classic mistake. Ask: what happens if you rotate before you move, versus move before you rotate? Try it on screen. Order matters here too.

## Slide 7
PRECEDENT — THE MASSING DIAGRAM
One drawing per operation. The sequence is the argument.
BIG MASSING DIAGRAM
Add: a sequential massing diagram, one axo per move.
WHAT MAKES IT WORK
One operation per frame. Never two.
The same viewpoint every frame, so the change is the only thing moving.
The moved or removed part is marked — colour, arrow, ghost.
It reads left to right without a caption.
Your diagram is graded on whether the sequence can be read — not on how the building looks.
Notes: Show three or four examples, good and bad. The bad ones usually change viewpoint between frames, or show two moves at once. Ask them to name the operation in each frame before you say it.

## Slide 8
ISSUED TODAY
0.1 — PROCEDURE: DIAGRAM + INSTRUCTIONS
DUE CLASS 4 — SEP 15 / 8%
Take an existing building. Rebuild its massing as a sequence of primitives and Booleans. Then document that sequence twice.
01
THE DIAGRAM
A sequential axonometric set — one drawing per operation — plus one larger final isometric with human scale, context, shadows and annotation.
02
THE INSTRUCTIONS
A written procedure another person could follow to rebuild your object without ever seeing your model.
BOTH ON ONE 17" × 11" SHEET, IN YOUR VISUAL IDENTITY.
Notes: Say it plainly: the diagram and the instructions carry equal weight. A beautiful diagram with vague instructions fails half the assignment.

## Slide 9
REQUIREMENTS
Counting these earns a C. The rest is judgement.
5+
Boolean operations
4+
distinct primitive types
2+
translations
1+
rotation
1
precedent analysis — 2–3 sentences on why the massing reads as a sequence
Operation history intact and demonstrable. No imported or downloaded models.
Notes: The C-floor line matters — say it out loud. Hitting these numbers is not the assignment, it's the entry price. No downloaded models: they will try. It defeats the whole exercise.

## Slide 10
THE NOTATION
Write the procedure as pseudocode. Formal enough to be unambiguous, plain enough to read aloud.
PRIMITIVES
box(x, y, z)
cylinder(r, h)
sphere(r)
cone(r, h)
TRANSFORMS
move(s, x, y, z)
rotate(s, axis, deg)
scale(s, factor)
BOOLEANS
union(a, b)
subtract(a, b)
intersect(a, b)
THREE RULES
Every shape is created centred on the origin (0, 0, 0). Move it from there.
Units are abstract. No millimetres, no metres — 3 units, half the width.
Every step assigns a name, so the order of a subtraction is never in doubt.
This is real: OpenSCAD is a working language built on exactly these operations.
Notes: Why formal notation and not plain English: LeWitt's instructions were ambiguous on purpose — different executors, different drawings. Yours must produce ONE result. Named assignment is the fix for the A−B / B−A problem from the Booleans slide. Origin-centred is the fix for 'where is it?' — every position is stated as a move from a known place. Mention OpenSCAD. Some of them will go and try it, which is a good outcome.

## Slide 11
WORKED EXAMPLE
Four operations. Read it, then draw what it makes.
PROCEDURE
base = box(6, 4, 3)
tower = box(2, 2, 6)
tower = move(tower, 2, 0, 3)
void = cylinder(r=1, h=5)
void = move(void, -1.5, 0, 0)
mass = union(base, tower)
result = subtract(mass, void)
WHAT THIS FIXES
ORDER
subtract(mass, void) can only mean one thing.
POSITION
Every shape starts at the origin, so a move is the whole story.
REUSE
A named step can be referred to later — mass is used, not rebuilt.
READING
Anyone can execute it. That is the test at Class 5.
Your sheet carries BOTH: the axonometric sequence, and the procedure that produces it.
Notes: Read it aloud line by line and have them sketch it. Two minutes. Then ask what is STILL ambiguous — e.g. which axis is the cylinder's height along? Does 'move' use the centre? That residue is what the Class 5 exchange will expose. Perfect notation still needs care.

## Slide 12
CHOOSING YOUR OBJECT
Pick badly and the rest of the assignment is impossible.
ORTHOGONAL MASSING
Boxes, slabs, stacked volumes. Right angles.
NO COMPLEX CURVES
If you cannot get there with primitives, it is the wrong building.
5–10 CLEAR MOVES
Too simple is boring. Too complex will not resolve in five Booleans.
APPROVED OBJECT LIST
Add: 6–8 buildings that work. Students may propose others for approval.
Notes: Have the list ready — this is the single biggest failure point in the assignment. If someone picks a building that cannot be described in five Booleans, the peer exchange at Class 5 fails for reasons that aren't their fault. Anyone proposing their own must clear it with you before they leave today.

## Slide 13
WHAT HAPPENS TO THIS WORK
Three things, and they are not all at once.
CLASS 4
SEP 15
Sheet due — diagram and instructions.
CLASS 5
SEP 22
Instructions exchanged. You build a classmate's object from their written procedure alone. The gap between the two results is the finding.
CLASS 8
OCT 13
Your object, 3D printed at small scale, presented at the Midterm. No supports — orientation is your only lever.
Notes: Flag the print now, not in October — the geometry they build today has to be printable. No supports means overhangs are their problem to design around. Say it today so it shapes the model.

## Slide 14
NOW — BUILD IT
Rest of the session: start your operation tree with help in the room.
✓
Object chosen and approved
✓
First three primitives placed
✓
At least one Boolean working
✓
Operation history intact — nothing collapsed to a mesh
LEAVE WITH A WORKING TREE.
Notes: Circulate. The two failures to catch early: collapsing to a mesh, and picking an object that won't resolve. Don't let anyone leave without an approved object.

## Slide 15
BEFORE NEXT CLASS
WATCH
Tutorial 0.2 — 3D printing. Manifold geometry, orientation, supports, layer height, slicing. Sent tonight.
CHECK
FabLab Safety Orientation must be complete by the end of today. Without it you cannot use any machine.
BUILD
Keep going on 0.1. Bring your tree next week — we prepare prints in class.
WRITE
Draft your instructions. Read them aloud to someone who has not seen the model.
Notes: The 'read them aloud to someone' instruction is the cheapest possible test and they will skip it. Say it twice.