## Slide 1
CLASS 03 / SEP 8
3D PRINTING
GEOMETRY THAT SURVIVES CONTACT WITH A MACHINE
MOSTLY A WORKING SESSION / BRING YOUR MODEL
Notes: Short front section, then prepare prints with help in the room.\nEveryone should leave with a sliced file in the queue, or a clear reason why not.

## Slide 2
WHAT THE MACHINE DOES
One thing, repeatedly. Everything else follows from this.
A NOZZLE DRAWS ONE FLAT LAYER,
THE BED DROPS, IT DRAWS THE NEXT.
nozzle
bed
IT BUILDS UPWARD, NEVER SIDEWAYS
Material can only be placed on material that is already there.
LAYERS ARE THE WEAK DIRECTION
A print snaps between layers long before it snaps across one.
EVERY DECISION IS A TIME COST
Finer layers, more material, more supports — all of it is hours on a shared machine.
Notes: The first fact is the one everything else hangs off. Say it, then use it three times today.\nSecond fact matters for their 0.1 print — a thin tower printed upright snaps at the layer line.

## Slide 3
MANIFOLD OR IT DOES NOT PRINT
A model can look perfect on screen and be meaningless to a slicer.
WATERTIGHT
No gaps. Every edge is shared by exactly two faces. If water could leak out, it is not a solid.
NO SELF-INTERSECTION
A shape that passes through itself has no unambiguous inside. The slicer cannot decide what to fill.
NORMALS OUTWARD
Every face has a front and a back. A flipped face tells the slicer that outside is inside.
CHECK BEFORE YOU SLICE. A BOOLEAN THAT LEFT AN OPEN EDGE IS THE MOST COMMON CAUSE OF A FAILED FILE.
Notes: Demo a broken Boolean live: leave a face open, run it through the slicer, show the nonsense it produces.\nThen show the repair. This is the single most useful five minutes of the session.\nName the check tool in whichever environment they're using — 3D Print Toolbox in Blender, Check/ShowEdges in Rhino.

## Slide 4
OVERHANGS
Each layer needs something under it. How much is the whole question.
VERTICAL
Every layer sits fully on the one below. Perfect.
45°
Half of each layer is supported. This is about the limit.
STEEP
Most of the layer hangs in air. It will droop or fail.
THE 45° RULE: BEYOND ABOUT 45° FROM VERTICAL, A SURFACE NEEDS SUPPORT — OR A DIFFERENT ORIENTATION.
Notes: The stacked-rectangle drawing is the honest explanation — each layer is offset from the one below, and past about half a layer width there is nothing holding the edge up.\n45° is a rule of thumb, not physics. Bridging across a gap behaves differently from a slope.\nAsk them to find the worst overhang in their own model before they leave.

## Slide 5
THE LETTER TEST
Four letters, four printing conditions. Find yours in your own model.
H
PRINTS FINE
BRIDGE
The crossbar spans between two legs that are already there. Anchored at both ends, so it can stretch across.
V
FINE TO 45°
SLOPE
Each layer steps outward a little. Gentle is fine; past about 45° from vertical it starts to droop.
T
DROOPS
CANTILEVER
The arms start in mid-air and are anchored at one end only. Nothing to stretch to.
i
IMPOSSIBLE
ISLAND
The dot begins with nothing underneath it at all. There is no version of this without support.
A BRIDGE IS ANCHORED AT BOTH ENDS. A CANTILEVER IS NOT. AN ISLAND IS ANCHORED TO NOTHING. THAT IS THE WHOLE DIFFERENCE.
Notes: Print these four letters beforehand and pass them around — the H bridge sags slightly, the T arms curl, the i dot is a blob on the bed. Nothing communicates it faster. Then: everyone find the H, V, T and i in their own model. Whoever has an i has a problem to solve today. This test comes from García Cuevas and Pugliese, Advanced 3D Printing with Grasshopper.

## Slide 6
ORIENTATION IS YOUR ONLY LEVER
Same geometry. Two ways to place it. Very different prints.
AS MODELLED
support
Overhang under the arm. Needs support, which costs material, time, and a scarred surface where it is removed.
ROTATED
The same arm now sits on the bed. No support, faster, cleaner face — and stronger, because the load is not across a layer line.
NO SUPPORTS ARE PERMITTED ON THE 0.1 PRINT. IF IT CANNOT PRINT UNSUPPORTED IN ANY ORIENTATION, CHANGE THE GEOMETRY.
Notes: The ban is pedagogical, not arbitrary — with supports off, orientation is the only variable, which is the fastest way to learn what it does.\nAnd revising the geometry to make it printable is a legitimate outcome. Say that clearly or they will panic.\nOrientation diagram is a required part of the 0.1 sheet: chosen orientation, the overhangs it produces, why it beat the alternative.

## Slide 7
WHAT THE SLICER DOES
Turns a solid into a list of moves. This is the same idea as Module 2.
01
CUT INTO LAYERS
The solid is intersected by a stack of horizontal planes.
02
OUTLINE EACH LAYER
Each intersection becomes a closed curve — the perimeter.
03
FILL THE INSIDE
Infill pattern and density. Usually 10–20%, not solid.
04
ORDER THE MOVES
Perimeters, infill, travel. Written out as G-code.
SOUND FAMILIAR?
Intersect a solid with a stack of planes. Keep the profiles. Order them.
That is Module 2 — and it is what a slicer has been doing all along.
LIVE NOW — we slice one object together and read the preview: layer count, print time, material, where the supports would go.
Notes: Slice something live and step through the preview layer by layer. Show the first layer, a mid layer, and the top.\nThe Module 2 connection is worth flagging out loud — they will meet contouring again in six weeks and this is the same operation.\nShow the time estimate and the material estimate. That is what makes the production plan real later.

## Slide 8
FOUR SETTINGS
Everything else can stay at default for this print.
LAYER HEIGHT
0.2–0.3 mm
Finer looks better and takes proportionally longer. Draft is fine for 0.1.
INFILL
10–40%
Prints are hollow with a lattice inside. Solid is almost never needed.
WALLS / PERIMETERS
2–3
This, not infill, is what makes a print feel solid.
SUPPORTS
OFF
Not permitted for 0.1. Solve it with orientation.
Notes: Resist tuning. They will want to change everything; almost all of it makes the print worse or longer.\nWalls versus infill is the useful one — students always crank infill to 100% and wonder why it takes nine hours.

## Slide 9
PRINT IT OR CUT IT
Printing is not the default. It is the expensive option.
CUT IT
Prismatic — one profile, extruded
Flat, or made of flat pieces
Repeated many times
Larger than your hand
Site model massing: stacked chipboard
Minutes per sheet. Twenty buildings at once.
PRINT IT
Doubly curved — a vault, a shell
Undercuts a blade cannot reach
Detail in all three axes at once
Small and intricate
One-off with no flat description
Hours per object. One at a time.
THE TEST: can the object be described as a stack of flat profiles, or one profile extruded? Then cut it. A simple box printed is a box you waited six hours for.
Notes: The site model example is the one that lands. A block of massing models is twenty boxes — laser them from chipboard in one pass, stack and glue. Printed, that is days of machine time for a worse object. This matters in Module 2 versus Module 3: 2.2 is cut because sections are flat; 3.2 is printed because a vault panel is doubly curved and has no flat description. Ask them which their 0.1 object would be if it were not a required print. Most would be cut.

## Slide 10
FABLAB — HOW THIS WORKS HERE
Machines are shared. The rules exist so everyone gets a print.
ORIENTATION COMPLETE
No Safety Orientation, no machine access. This was due at the end of Class 2.
NEVER TOUCH THE HOT END
The nozzle runs around 200–250°C and does not look hot. The bed is hot too.
DO NOT RESTART SOMEONE'S PRINT
If a job looks like it is failing, tell staff. Do not intervene.
QUEUE IS FIRST COME
A print that finishes at 3am still finishes. One that starts at the deadline does not.
`[CONFIRM WITH DIEGO: BOOKING METHOD, FILE NAMING, PICK-UP, MATERIAL ALLOCATION]`
Notes: Replace the bottom bar with the actual FabLab procedure before you teach this.\nBe specific about file naming — it is the difference between a print they can find and one they cannot.

## Slide 11
SIX WAYS IT GOES WRONG
Learn to name the failure. Naming it is most of the diagnosis.
WARPING
Corners lift off the bed and the base curves.
CAUSE
Cooling shrinkage beats bed adhesion.
FIX
Clean bed, add a brim, keep drafts off it.
ELEPHANT'S FOOT
The bottom few layers bulge out wider than the rest.
CAUSE
Nozzle too close, or bed too hot.
FIX
Slicer setting — or chamfer the base yourself.
STRINGING
Fine hairs between separate parts of the print.
CAUSE
The nozzle oozes while travelling.
FIX
Retraction on. Fewer travel moves — ordering again.
LAYER SEPARATION
The print splits cleanly along a layer line.
CAUSE
Weak bond, or the load runs across layers.
FIX
Reorient so stress runs along layers, not across.
DROOP
An overhang sags into the space below it.
CAUSE
Nothing underneath to build on.
FIX
Orientation. If that fails, change the geometry.
SPAGHETTI
The nozzle draws in mid-air. A nest of filament.
CAUSE
The part came off the bed part-way through.
FIX
Adhesion. Check the first layer before walking away.
Notes: Pass around real failed prints for as many of these as you have — a photo does not communicate a delamination or a support scar. Stringing is worth a beat: the cause is travel moves, which is the same ordering problem as the plotter demo in Class 6. Same lesson, different machine. Tell them to keep their failures. A print that failed and was correctly diagnosed is worth more in the booklet than one that worked by luck.

## Slide 12
FOR 0.1
YOUR PRINT
PRESENTED AT THE MIDTERM — CLASS 8, OCT 13
60 mm
maximum bounding box
NO SUPPORTS
orientation is the only lever
DRAFT
layer height — this is a test, not a showpiece
1 DIAGRAM
chosen orientation, the overhangs it produces, why not the alternative
Assessed on printability and on your reasoning. Not on craft — that is 3.2's job.
Notes: Say the assessment basis plainly. A rough print with a good orientation argument passes. A pretty print they cannot explain does not.\nNo credit for 0.1 without the print — repeat that.

## Slide 13
NOW — PREPARE YOUR PRINT
Rest of the session: get a sliced file into the queue with help in the room.
✓
Model checked — manifold, watertight, normals consistent
✓
Scaled to fit within 60 mm
✓
Orientation chosen and justified — no overhang past ~45°
✓
Sliced. Print time and material noted.
✓
File named and submitted to the queue
LEAVE WITH A FILE IN THE QUEUE.
Notes: Circulate. The two things to catch: non-manifold geometry, and models scaled wrong so print time is absurd.\nAnyone who cannot get a printable orientation should revise geometry today, not next week.

## Slide 14
BEFORE NEXT CLASS
WATCH
Tutorial 1.1 — arrays. Linear, grid, hexagonal, along a curve. Sent tonight.
FINISH
0.1 is due next class: the axonometric sequence, the procedure, the precedent analysis.
CHECK
Your print is in the queue. It is presented at the Midterm, not next week — but the file has to exist.
READ
Your own procedure, out loud, to someone who has not seen the model. Fix what they cannot follow.
Notes: 0.1 is due next class — make sure nobody thinks the print buys them an extension on the sheet.\nModule 1 starts next week, so the pace picks up.