## Slide 1
CLASS 04 / SEP 15
MODULE 1 — FIELDS
ARRAYS
PARAMETRIC BEGINS HERE
0.1 + 0.2 DUE
1.1 ISSUED TODAY / ARRAYS + ATTRACTORS
Notes: Collect 0.1 and 0.2 at the start. Quick pin-up if time — full exchange is next week.\nToday is the paradigm shift: everything from here has parameters driving it.

## Slide 2
WHERE WE JUST MOVED TO
Module 0 is finished. The ground has changed.
PROCEDURAL
MODULE 0 — DONE
A fixed sequence of operations.
You defined the steps.
One expected result.
PARAMETRIC
MODULES 1–3 — NOW
Relationships between inputs and form.
You define the rules of variation.
A family — you know the range,
not each member.
An array on its own is still procedural — repeat this N times. It becomes parametric the moment a parameter governs how the copies differ.
Notes: Do not skip this slide. Students treat Module 1 as 'now we make patterns'. The real content is the transition from repetition to controlled variation.\nThe bottom line is the whole module in one sentence.

## Slide 3
AN ARRAY IS A LIST OF POSITIONS
Not a command that duplicates things. A list you compute, then place geometry at.
INDEX → POSITION
i = 0 → p = start
i = 1 → p = start + step
i = 2 → p = start + 2 × step
i = 3 → p = start + 3 × step
p[i] = start + i × step
YOU ALREADY KNOW THIS
Move is addition. An array is move, repeated, with the amount driven by the index.
The index is the only new idea: a counter that tells each copy how far along the sequence it is — and therefore how different it should be.
The index is what makes variation possible. Without it every copy is identical, because nothing distinguishes one from another.
Notes: Call back to the Class 2 arithmetic slide — move is addition. Nothing new has happened except the counter.\nThe index point is the bridge to attractors next week: index tells you WHERE in the sequence, distance tells you HOW FAR from something. Both are just numbers driving a property.

## Slide 4
FOUR ARRAYS
Same idea, four ways of generating the list.
LINEAR
p[i] = p₀ + i·d
GRID
p[i][j] = p₀ + (i·dx, j·dy)
HEX
offset odd rows by dx/2
ON CURVE
p[i] = curve at t = i/n
A grid is a list of lists — two counters instead of one. Hold that thought; it returns in Module 3 as a panel field.
Notes: Build each one live from the same starting point, so they see it is one idea with four list-generation strategies.\nOn curve is the one they will struggle with: the list comes from dividing the curve, not from adding a fixed step. The spacing is in curve parameter, not distance — worth demonstrating on a curve with uneven curvature.

## Slide 5
REPETITION IS NOT THE POINT
The same grid, twice. One is a pattern. The other is a system.
REPETITION
PROCEDURAL
Every element identical. The index is generated and then ignored.
VARIATION
PARAMETRIC
Size driven by the index. The same list, now doing work.
1.1 REQUIRES VARIATION. A FIELD OF IDENTICAL ELEMENTS DOES NOT MEET THE ASSIGNMENT.
Notes: The right-hand grid uses r = f(index). Nothing else changed.\nThis is the single most important idea in Module 1 — say it, show it, and repeat it when you brief 1.1.

## Slide 6
ARRAYS IN ARCHITECTURE
Screens, façades, structure, aggregation. Look for the rule, not the image.
SCREEN / MASHRABIYA
Add: a perforated screen with graded aperture.
REPEATING FAÇADE
Add: a façade whose module varies across the elevation.
STRUCTURAL AGGREGATION
Add: a structure built from one repeated element.
FOR EACH ONE, ASK THREE QUESTIONS
What is the module? What generates the positions? What varies across the field, and what drives it?
Notes: Three questions, every precedent, all module long. They are also the questions their own precedent analysis must answer.\nPush past 'it looks nice' — make them name the rule that would regenerate it.

## Slide 7
ISSUED TODAY
1.1 — ARRAYS + ATTRACTORS
DUE CLASS 6 — SEP 29 / 8%
An array organizes points. An attractor differentiates them. This assignment is about what happens when you combine the two — a matrix of approaches, where different array types are driven by different attractor types.
SINGLE POINT
MULTIPLE POINTS
CURVE
LINEAR
GRID
HEX
ON CURVE
PICK 3 CELLS.
ANY THREE.
Notes: The matrix makes the assignment concrete — 16 possible combinations, they pick three.\nEmphasise that the comparison between their three is the point. Same technique, different graphic consequence.

## Slide 8
REQUIREMENTS
Counting these earns a C. The rest is judgement.
3+
array/attractor combinations, drawing on all array types taught
3
attractor types across the set: single point, multiple points, curve
3+
parameters driven by attractor distance — scale, rotation, density, height, colour
1,000+
elements in at least one composition
1+
composition resolved spatially in 3D
3 VIEWS
of one combination: isometric, close-up, eye-level
1
precedent analysis — 2–3 sentences: module, positions, what varies
Arrays and falloff authored. Array add-ons, scatter tools and preset falloff plugins are prohibited.
Notes: The prohibition is enforced by explanation, not by auditing files — they submit a short written statement of how their falloff is computed.\nMinimum 2 sheets. Say the C-floor line again.

## Slide 9
NOW — BUILD THE ARRAYS
Rest of the session: all four array types, working, from one starting point.
✓
Linear array with a controllable count and spacing
✓
Grid array — two counters, not one array duplicated
✓
Hexagonal array — odd rows offset by half the spacing
✓
Array along a curve you drew yourself
✓
One property driven by the index, so the set is not uniform
THE LAST ONE IS THE ASSIGNMENT. THE OTHERS ARE PRACTICE.
Notes: Watch for students duplicating a linear array to fake a grid. Make them build the second counter.\nAnyone finished early: drive spacing by the index instead of scale, and see how differently it reads.

## Slide 10
BEFORE NEXT CLASS
WATCH
Tutorial 1.2 — attractors. Single point, multiple points, curve. Distance, falloff, remapping. Sent tonight.
BRING
Your working arrays. Next week we drive them with attractors, so bring a file you can build on.
BRING
Your 0.1 procedure, printed. Next class you build a classmate's object from theirs.
LOOK
One precedent for 1.1. Be ready to name the module, the positions, and what varies.
Notes: The printed procedure is essential — the exchange does not work if it is on a laptop.\nRemind them the 0.1 print is due at the Midterm, not next week, but the file should already be queued.