## Slide 1
CLASS 05 / SEP 22
THE EXCHANGE
ATTRACTORS
FIRST HALF: BUILD A CLASSMATE'S
SECOND HALF: DISTANCE DRIVES FORM
MODULE 1 / PARAMETRIC / 1.1 DUE NEXT CLASS
Notes: Exchange first while everyone is fresh — it needs concentration.\nAttractors after the break, then clinic time on 1.1.

## Slide 2
THE EXCHANGE
You will build someone else's object from their words alone.
01
SWAP
Hand your printed procedure to the person opposite. Keep your diagram — they do not get to see it.
02
BUILD
25 minutes. Follow the procedure exactly as written. Do not interpret generously.
03
STOP WHERE IT BREAKS
If a step is ambiguous, stop, write down what was unclear, then make the most literal reading and continue.
04
COMPARE
Put your result next to the author's diagram. The difference is the finding.
DO NOT TALK TO THE AUTHOR. IF YOU CAN ASK THEM, THE PROCEDURE IS NOT BEING TESTED.
Notes: Enforce the no-talking rule hard. It is the whole experiment.\n'Do not interpret generously' is the instruction that makes it work — students want to be kind and fill in gaps. Tell them being literal is the favour.

## Slide 3
WHAT TO RECORD
Both of you write this down. It goes in the booklet.
AS THE BUILDER
Every step where you had to guess
What you assumed, and why
A photo of what you produced
AS THE AUTHOR
Which steps were misread, and how
What you meant, in one sentence
The rewritten step that fixes it
THE USUAL SUSPECTS
Which axis is the cylinder's height along? Does move() apply to the centre or a corner? Which way is positive rotation? Is the subtraction the right way round?
Notes: The usual-suspects list is a prediction. Read it out before they start and see how many they hit.\nFormal notation removed most ambiguity — what is left is precise and fixable, which is exactly the point. Say that in the debrief so it does not feel like a failure.

## Slide 4
AN ATTRACTOR IS A NUMBER
For every point: how far is it from something? Use that number to drive a property.
THE WHOLE IDEA
for each point p:
d = distance(p, attractor)
size = f(d)
That is it. Everything else is
a choice of f.
INDEX told you where in the sequence. DISTANCE tells you how far from something. Both are just numbers driving a property — that is the only idea in this module.
Notes: Write the three lines on the board. Students think attractors are a component; they are a subtraction and a function.\nThe closing line ties Class 4 to today — index and distance are interchangeable as drivers. Somebody should try index-driven and distance-driven versions of the same field.

## Slide 5
THREE KINDS
Same maths. What changes is what you measure the distance to.
SINGLE POINT
distance(p, a)
MULTIPLE POINTS
min over all attractors
CURVE
distance to nearest point on the curve
Notes: Point out that the third one has no marker — the attractor is the whole curve, and the distance is to its nearest point.\nMultiple points is where the real decision is, and it is on the next slide.

## Slide 6
FALLOFF IS THE FUNCTION
f is your decision. It is where the graphic quality actually comes from.
LINEAR
distance →
v = d
Even change all
the way across.
INVERSE
distance →
v = 1 / d
Sharp near the
attractor, flat far off.
SMOOTH
distance →
eased
Soft at both ends.
Usually the best-looking.
THRESHOLD
distance →
on / off at a cut
No gradient at all.
Two populations.
Two students with the same attractor and different falloff produce completely different images. This is a design decision, not a setting.
Notes: Have them try all four on one field in ten minutes. The difference is dramatic and it convinces better than any explanation.\nThreshold is worth naming as a legitimate choice — it produces figure/ground rather than gradient, which is a different graphic proposition.

## Slide 7
REMAP
Distance comes out in model units. Your property needs a specific range. Remap is the bridge.
THE OPERATION
t = (d − dmin) / (dmax − dmin)
out = outmin + t × (outmax − outmin)
d 0 … 8.4 units
out 0.1 … 1.0 radius
SUBTRACT. DIVIDE.
MULTIPLY. ADD.
Nothing here is new. It is the arithmetic from Week 2, applied to a distance instead of a coordinate.
Get the ranges wrong and everything is the same size, or one element swallows the sheet.
1.1 REQUIRES YOUR REMAP RANGES DOCUMENTED ON THE SHEET — INPUT RANGE IN, OUTPUT RANGE OUT.
Notes: Remapping is the single most common place students get stuck, and it always looks like a plugin problem when it is an arithmetic problem.\nDiagnostic question when a field looks flat: what is your actual distance range? Usually they are mapping 0–100 into 0–1 and everything lands at 0.02.

## Slide 8
TWO ATTRACTORS, THREE ANSWERS
With more than one attractor each point has a list of distances. How you reduce it is a design choice.
MIN
nearest one wins
MAX
farthest one wins
MULTIPLY
both, multiplied
Same two attractors in all three. Only the reduction changed — territories, a single central blob, or two peaks with a pinch between them.
Notes: This is the slide worth the most in the whole session. Multiple-point attractors are usually taught as 'use the closest one' and nothing else.\nMin gives you cell-like territories. Sum gives blobs and merging. Average pulls everything toward the midpoint.\nAnyone doing the multiple-point cell of the matrix should try all three.

## Slide 9
UNDERNEATH, IT IS LISTS
Points, distances, sizes. Three lists, same length, same order.
POINTS
[0]
p₀
[1]
p₁
[2]
p₂
[3]
p₃
[4]
p₄
DISTANCES
[0]
2.1
[1]
0.4
[2]
5.8
[3]
3.2
[4]
1.0
SIZES
[0]
0.42
[1]
0.95
[2]
0.10
[3]
0.28
[4]
0.71
PARALLEL LISTS
Item [2] in every list describes the same element. Break that correspondence — by sorting or culling one of them — and the sizes attach to the wrong points.
That is what “managing lists” means, and it is next week's whole subject.
When a field looks scrambled, it is almost always a list that got reordered somewhere upstream.
Notes: This is the bridge to Module 2 — contouring is entirely a list-management problem.\nThe diagnostic line at the bottom is worth memorising; it is the answer to half the questions you will get during the clinic.

## Slide 10
WHEN TWO LISTS MEET
4 points, 2 attractors. How do they pair up? The software decides — unless you decide.
LONGEST LIST
p0
p1
p2
p3
a0
a1
POINTS
ATTRACTORS
4 results
The short list repeats its last item to keep up.
SHORTEST LIST
p0
p1
p2
p3
a0
a1
POINTS
ATTRACTORS
2 results
Stops when the short list runs out. Two points get nothing.
CROSS REFERENCE
p0
p1
p2
p3
a0
a1
POINTS
ATTRACTORS
8 results
Every point against every attractor. This is usually what you want.
This is why your two-attractor field went wrong. Longest List is the default, and it silently ignored your second attractor for most points.
Notes: Almost every broken multi-attractor field traces back to this slide. The default is Longest List and it produces something that looks plausible but is wrong. Cross Reference gives 8 results for 4 points — which then have to be reduced back to 4 (min, max, multiply, from the previous slide). Say that connection out loud. Note: Cross Reference may be used ONCE per definition in this course. Beyond that, use graft — next slide.

## Slide 11
GRAFT, FLATTEN, WRAP
Three operations that change list structure rather than list contents.
GRAFT
one list → one branch each
a
{0} a
b
{1} b
c
{2} c
Each item becomes its own branch, so the next operation treats them separately instead of pairing them off.
FLATTEN
many branches → one list
{0} a
{1} b
{2} c
a
b
c
The opposite. Useful at the end — destructive in the middle, because it throws away the structure you built.
WRAP
index past the end → back to the start
i mod n
index
0
1
2
3
4
5
6
7
wrapped (n = 4)
0
1
2
3
0
1
2
3
Item 5 of a 4-item list is item 1. This is how you join the last element back to the first.
WRAP IS WHY A CONTOUR CLOSES. Connect point [i] to point [i+1] and the last one has no partner — unless the index wraps. That is Module 2 in one line.
Notes: Graft is the operation students copy without understanding. Frame it as: stop pairing these off, handle each one separately. Flatten is the one they overuse — it fixes the symptom by destroying the structure. Say: if flattening fixed it, you had a matching problem, not a flatten problem. Wrap is modulo, which is the same arithmetic framing as Week 2. Demonstrate it on a closed polyline: without wrap you get an open chain, with wrap you get a closed loop. That closing behaviour is exactly what contouring needs next week.

## Slide 12
ATTRACTORS IN ART, DESIGN, ARCHITECTURE
Same three questions: what is the module, what generates the positions, what drives the variation.
ART / GRAPHIC
Add: a field work — op art, generative graphics, poster.
PRODUCT / OBJECT
Add: an object with graded perforation or density.
ARCHITECTURE
Add: a façade or screen driven by an attractor logic.
AND ONE MORE QUESTION
Where is the attractor? Sometimes it is a door, a view, a structural point, the sun. Sometimes it is nowhere — chosen purely for the image.
Notes: The last question is the one that separates an architectural use from a decorative one. Both are legitimate here — but they should know which they are doing.\nYour own precedent analysis for 1.1 must answer it.

## Slide 13
NOW — 1.1 CLINIC
Due next class. Bring your problems to the front.
✓
Three cells of the matrix chosen — which arrays, which attractors
✓
All three attractor types working somewhere in the set
✓
3+ parameters driven by distance — not just scale three times
✓
Remap ranges written down, ready to put on the sheet
✓
One composition over 1,000 elements, one resolved in 3D
✓
Precedent chosen and the three questions answered
THREE DIFFERENT SCALES IS NOT THREE PARAMETERS.
Notes: The bottom line catches the most common shortcut — they drive scale, then scale again, then scale in a third array, and call it three parameters.\nRotation, density, height and colour are all sitting there unused.

## Slide 14
BEFORE NEXT CLASS
FINISH
1.1 is due next class. Two sheets minimum, in your visual identity.
WATCH
Tutorial 2.1 — contouring and list management. Generating contours, then reordering, filtering and reconnecting them.
WRITE
Your mechanism statement for 1.1: how your falloff is computed, in your own words.
FIX
The step in your 0.1 procedure that your partner could not follow. One rewritten line.
Notes: The rewritten 0.1 line is small but it closes the loop on the exchange — and it is exactly the kind of revision the booklet grade rewards.