## Slide 1
CLASS 12 / NOV 10 / U09
DISCRETIZING
GEOMETRY
P4 CONTINUES — FROM A CONTINUOUS VOLUME TO ORDERED PARTS
P4a DUE
P4b ISSUED TODAY

## Slide 2
TODAY
Three things change hands before we cut a single section.
DUE
P4a — SDF VOLUME
DUE WEEK 12 — Nov 10 / 14%
Two sheets as PDF, plus the editable field graph with the source fields retained.
CHECKPOINT
BOOK — PROGRESS CHECK
WEEK 12 — Nov 10
Bring a booklet spread and contents list for an ungraded progress check. Ungraded.
ISSUED
P4b — SLICES
DUE FINAL / 14%
Your P4a volume becomes laser-cut parts. Brief at the end of the class.
THE VOLUME YOU SELECTED ON P4a SHEET 2 IS THE ONE YOU SLICE. DO NOT START A NEW ONE.

## Slide 3
FOUR DECISIONS BEFORE ANY CUT
A slice set is not a setting. Each of these changes what the assembly says about the volume.
PLANE
What cuts the volume: a plane, repeated. The contour is where they meet.
DIRECTION
Which way the planes face. It decides which profiles you see.
INTERVAL
The distance between planes. It sets the gaps, the light and the part count.
ORDER
Which slice is first. The order becomes the labels and the assembly.
ONE VOLUME, 12 HORIZONTAL PLANES
01 at the bottom · 12 at the top
P4b asks for at least 12 ordered slices. Twelve is the floor, not the target.

## Slide 4
COMPARE BEFORE YOU COMMIT
Same volume, three slice sets. P4b asks you to compare two directions or two intervals.
HORIZONTAL · WIDE
Reads as a stack. Clear profile, open gaps.
VERTICAL · WIDE
Reads as fins. The silhouette changes with view.
HORIZONTAL · TIGHT
Nearly continuous. More parts, less light.
LOST
Everything between the planes. Curvature becomes steps.
GAINED
Gaps, light and a reading of the form. Parts a machine can cut.

## Slide 5
SLICES ARE DESIGNED PARTS
In Week 3 a slicer made the layers for you. Here, every section is a part you decide on.
PRINTER LAYERS
Generated by the slicer, not by you.
Hundreds of them, fused into one object.
You never see one on its own.
SECTION PARTS
Chosen: direction, interval, order.
A countable set, each with a thickness, a label and a place in the assembly.
Every one is visible in the finished piece.
DECIDE WHICH CURVES ARE PART BOUNDARIES BEFORE YOU ASSIGN THICKNESS OR SEND A MACHINE FILE.

## Slide 6
THE SEQUENCE
Steps 1 and 2 today. Steps 3 and 4 are next week's class.
01
Intersect the volume or its extracted boundary with a sequence of planes; order the resulting contour curves.
02
Compare two section directions and intervals, including the relationship between gaps, light and the reading of the form.
03
Close and clean the intended profiles; turn them into parts with material thickness and a clear registration system.
04
Test fit and kerf, then number, nest and fabricate the parts and document the assembly.

## Slide 7
THE SAME THING, WRITTEN OUT
Slice in order, then prepare each part. The loop is the same one you wrote for arrays.
sections = []
for k in range(count):
z = z0 + k * interval
sections.append(slice(volume, z)) # ordered, and order matters
for i, s in enumerate(sections):
s = offset(s, kerf / 2) # the blade has width
label(s, i)
nest(s, sheet)
WHAT IT MAPS ONTO
section plane
contour
interval
discretization
thickness
registration
kerf
nesting
THE FIRST LOOP IS TODAY. THE SECOND LOOP — KERF, LABEL, NEST — IS NEXT WEEK.

## Slide 8
ISSUED TODAY
P4b — DISCRETIZING AND LASER-CUT FABRICATION
DUE FINAL / 14%
Take the volume you selected in P4a and translate it into at least twelve ordered sections. Compare two directions or intervals, give the slices a thickness and a registration system, then laser-cut and assemble them within one sheet of material.
COMPARE
TWO SLICE SETS
Two directions or two intervals, from the same volume.
MAKE
12+ PARTS
Thickness, registration, labels, nesting. Within 300 mm.
SHOW
ONE PROCESS SHEET
Volume, sections, cutting layout, assembly, photographs.

## Slide 9
REQUIREMENTS — P4b
01
Use the selected P4a volume. Compare two section directions or intervals, then develop at least 12 ordered slices with material thickness and a registration system.
02
Fit the assembly within 300 mm on each axis and one confirmed material sheet. Test kerf and fit before the batch; label and nest every part.
03
Laser-cut and assemble the slices under FabLab procedures. Include test cuts and failed parts in the material allocation.
04
Present the assembly with one 17 x 11 inch process sheet showing the continuous volume, section sequence, cutting layout, assembly diagram and photographs.
05
Submit the editable source, cutting file and documentation. Regenerate fabrication files after any geometry or material change.
CHECKPOINT · WEEK 13 — Nov 17 — Review section directions, thickness, registration, fit/kerf test and cutting layout before production.
Visual documentation 20% · computational understanding 20% · technical execution 15% · fabrication quality 30% · experimentation 5% · requirements and identity 10%.

## Slide 10
NOW — CUT THE VOLUME
Rest of the class: sections from your P4a volume, compared before anything is chosen.
✓
P4a submitted, and your booklet spread and contents list checked
✓
Your selected volume sectioned by a sequence of planes
✓
The contours ordered, with slice 01 identified
✓
A second slice set: another direction or another interval
✓
The two sets set side by side, with a sentence on what each one shows
IF THE TWO SETS LOOK THE SAME, CHANGE MORE.

## Slide 11
BEFORE NEXT CLASS
NEXT
Week 13 (target Nov 17) — Parts for the laser cutter: registration, kerf and fit, labels and nesting.
BRING
A candidate slice set: at least 12 ordered contours, with the direction and interval written down, and your comparison of two sets.
CHECK
P4b checkpoint, Week 13 — Nov 17 (target): Review section directions, thickness, registration, fit/kerf test and cutting layout before production.
FIND
Your material: measure the sheet you plan to use and confirm its size and thickness with the FabLab before you design parts around it.