## Slide 1
CLASS 14 / NOV 24 / U10
FINAL
PRODUCTION
P4b AND BOOK — MAKE IT, PHOTOGRAPH IT, WRITE IT UP
NOTHING DUE
FINAL

## Slide 2
A PRODUCTION PLAN
Lab time is shared and limited. Write the sequence down before you book the machine.
01 CONFIRM
Sheet, thickness, fit and the cutting file.
02 TEST
Coupon and a few parts. Adjust. Regenerate.
03 CUT
The batch, from the regenerated file.
04 CHECK
Count and inspect every part against the list.
05 ASSEMBLE
In label order, dry first.
06 RECORD
Photograph each stage as it happens.
PLAN FOR
Lab availability · the time a batch takes · a spare part or two · a retest if the fit changes
TEST CUTS AND FAILED PARTS COUNT AGAINST YOUR ONE SHEET. KEEP BACKUP MATERIAL IN MIND.

## Slide 3
TEST BEFORE THE BATCH
A small cut now is cheaper than a sheet of parts that do not fit.
FIT
Cut the coupon from the production sheet. Confirm the slot that holds.
JOINT
Cut one registration joint: two slices and the spine, dowel or spacer.
SMALLEST
Cut the smallest and thinnest part. If it breaks, change the profile.
LABEL
Check the engraved numbers are legible and on the hidden face.
ANY CHANGE AFTER A TEST — GEOMETRY OR MATERIAL — MEANS YOU REGENERATE THE CUTTING FILE.
Keep every test piece. They are evidence for the process sheet.

## Slide 4
THE ASSEMBLY SEQUENCE
The order you sliced in is the order you build in. Draw it before you do it.
BEFORE GLUE
— Lay the parts out in label order
— Dry-fit the whole assembly on its registration
— Check the up and front marks on every part
— Fix a problem part now, not after it is glued
THE ASSEMBLY DIAGRAM
P4b asks for one on the process sheet.
Show the registration first, then the parts arriving in order. Number them as they are labeled.
Someone else should be able to build it from the diagram.
IF THE PARTS DO NOT GO TOGETHER IN LABEL ORDER, THE ORDER IS WRONG — NOT THE PARTS.

## Slide 5
PHOTOGRAPHING PHYSICAL WORK
The booklet shows the object through photographs. Treat them as drawings, with your GSM.
LIGHT
One soft main light from the side. The gaps between slices need shadow to read.
BACKGROUND
Plain, even and wider than the frame. Nothing else on the table.
SCALE
One view with a hand or a ruler, so the size is never in doubt.
SEQUENCE
The same angle at each stage: parts, test, half built, complete.
PHOTOGRAPH THE CSG PRINT TOO. BOOK ASKS FOR PHOTOGRAPHS AND CAPTIONS OF BOTH PHYSICAL PIECES.
Shoot more than you need, from the same position each time. Pick the set on the page, not on the camera.

## Slide 6
DOCUMENT THE REVISIONS
The booklet rewards substantive revision. Show what changed, not only the final state.
BEFORE
The version that was reviewed: sheet, file or part.
CHANGE
What you changed, in one sentence, with the parameter or step named.
WHY
The critique, test or failure that caused it.
AFTER
The revised result, shown at the same scale and angle.
KEEP
Dated file versions · test pieces · review notes · failed parts, photographed before you throw them away
A REVISION YOU CANNOT SHOW IS A REVISION THE REVIEW CANNOT SEE.

## Slide 7
FOUR PROJECTS, NINE ASSIGNMENTS
The booklet: 17 × 11 inch pages in your graphic standards. The GSM is a chapter, and it is also every page.
P1 GSM
GSM
Graphic Standards Manual
Applied to every page of the booklet, and also submitted as a separate revised PDF.
P2 CSG
P2a
CSG process and instructions
P2b
CSG 3D printed object
P3 PANELING
P3a
Descriptive geometry module
P3b
Arrays
P3c
Attractor: 2D field plotter drawing
P3d
Attractor: site analysis with Mixtli
P4 VOLUMETRIC DATA
P4a
SDF volume
P4b
Discretizing and laser-cut fabrication
FOR EACH: THE REVISED SHEET · THE PROCESS · WHAT CHANGED AFTER CRITIQUE · PHOTOGRAPHS FOR P2b AND P4b

## Slide 8
REMINDER — BOOK
Substantive revision 40% · documentation 35% · visual identity 25%.
01
Compile all four projects and nine assignments in revised form, using 17 x 11 inch pages and your graphic standards.
02
Include process diagrams, photographs and captions for the CSG print and laser-cut volume. Identify substantive revisions after critique.
03
Submit the booklet PDF, a separate revised GSM PDF, editable project files and dependencies, and required fabrication files.
04
Present the laser-cut assembly and the CSG print or its review documentation as directed. The exact final review slot remains to be confirmed.
DUE AT THE FINAL REVIEW · DECEMBER 10–16, 2026; EXACT REVIEW SLOT TO BE CONFIRMED / 11%

## Slide 9
NOW — PRODUCTION
Rest of the class: tests reviewed, production planned, booklet moving.
✓
Your fit and joint tests on the table, with what you changed
✓
The cutting file regenerated after the last test
✓
A written production plan with your lab time booked
✓
The assembly diagram drafted in label order
✓
One booklet spread revised, with a before-and-after
TEST, REGENERATE, THEN CUT. IN THAT ORDER.

## Slide 10
BEFORE NEXT CLASS
NEXT
Week 15 (target Dec 1) — Assembly follow-through, documentation and file checks. Review week: nothing is due.
MAKE
Cut the batch and assemble within your lab allocation. Photograph each stage from the same position.
BRING
The assembly as far as it has got, your photographs, and the booklet with every project in place.
CHECK
P4b checkpoint, Week 15 — Dec 1 (target): Review the assembled result, photographs and final booklet documentation.