## Slide 1
CLASS 03 / SEP 8 / U03
GEOMETRY
FROM SCRATCH
P1 CONTINUES — WHAT A SOLID IS MADE OF, UNDERNEATH
NOTHING DUE
P1b + P1c ISSUED TODAY

## Slide 2
POINT → LINE → EDGE → FACE → SOLID
Five steps, and each one is a list of the thing before it.
POINT
three numbers
[x, y, z]
LINE
two positions
[p1, p2]
EDGE
two vertices
[v1, v2]
FACE
ordered corners
[v1, v2, v3]
MESH
many faces
[f1, f2, f3…]
A POSITION IS NOT A DISPLACEMENT. THE SAME THREE NUMBERS MEAN DIFFERENT THINGS DEPENDING ON WHICH ONE YOU MEANT.
Nothing here is new geometry. It is the same collection, read at a different level: a face is a list of vertices, a mesh is a list of faces, and next week an array will be a list of copies.

## Slide 3
A FACE IS AN ORDERED LIST OF CORNERS
Same three vertices, two different faces. The order is the difference.
WINDING ORDER
v0
v1
v2
f = [v0, v1, v2]
normal → toward you
f = [v0, v2, v1]
normal → away
WHY IT MATTERS LATER
A flipped face tells a renderer the inside is the outside.
It tells a slicer there is nothing to fill.
Most failed prints this semester will start here, not at the printer.
CLOSED MEANS EVERY EDGE IS SHARED BY EXACTLY TWO FACES. CHECK IT BEFORE YOU BELIEVE IT.

## Slide 4
THE PYRAMID
Five vertices, eight edges, five faces. Built by hand, driven by three numbers.
WHAT YOU ASSEMBLE
5
VERTICES
four base corners and an apex
8
EDGES
four around the base, four to the apex
5
FACES
four triangular sides and the base
EXPOSED INPUTS
Width
Depth
Height
Three numbers, and the whole solid rebuilds. That is the entire point of the exercise.
DO NOT FORGET THE BASE FACE. A PYRAMID WITH FOUR SIDES AND NO BOTTOM IS NOT A SOLID.

## Slide 5
AND THEN IT GOES BACK INTO LAST WEEK'S FILE
The pyramid is not an exercise. It is the cutter for the study you already built.
01 BUILD IT
Five vertices, five faces, closed, with Width / Depth / Height exposed.
02 SUBTRACT IT
Cube minus pyramid. The same Boolean from Week 2, with your own solid.
03 DRIVE IT
Change the three inputs and show at least three settings of the result.
04 EXPLAIN IT
Face order, normals, closure — why it cuts cleanly instead of failing.
THIS IS WHY P1 IS ONE PROJECT AND NOT THREE ASSIGNMENTS.
Every project in this course does the same thing — the geometry you make in one milestone becomes the input to the next. You will never start from an unrelated object.

## Slide 6
THE SAME THING, WRITTEN OUT
A mesh is two lists. That is the entire idea, and it fits on one slide.
verts = [[-w, -d, 0], # 0
[ w, -d, 0], # 1
[ w, d, 0], # 2
[-w, d, 0], # 3
[ 0, 0, h]] # 4 apex
faces = [[0, 1, 4], [1, 2, 4],
[2, 3, 4], [3, 0, 4],
[0, 3, 2, 1]] # the base — do not forget it
pyramid = mesh(verts, faces)
result = difference(cube, pyramid)
WHAT IT MAPS ONTO
point
vector
parameter
vertex
line
edge
face
mesh
solid
normal
verts IS A LIST OF POSITIONS. faces IS A LIST OF INDICES INTO IT.

## Slide 7
ISSUED TODAY
P1b — MESH FROM SCRATCH
DUE WEEK 5 — Sep 22 / 7%
Build the solid from its parts, then take it back to the massing study and let it do work there. One sheet covers the whole ladder — point, line, edge, face, mesh — and ends with an annotated closed pyramid.
SHOW
THE LADDER
Point, line, edge, face, and the multiple-face exercise.
BUILD
THE PYRAMID
Width, Depth and Height exposed. Four sides and a base.
REUSE
AS A CUTTER
Back into the P1a study, at three parameter settings.

## Slide 8
REQUIREMENTS — P1b
Visual quality 35% · computational understanding 25% · technical execution 20% · experimentation 10% · requirements and identity 10%.
01
One sheet showing point, line, edge, face and the multiple-face mesh exercise, with an annotated closed pyramid.
02
Build four base corners and an apex with Width, Depth and Height exposed; include all four side faces and the base.
03
Reuse the pyramid as a Boolean cutter in the previous study and show at least three parameter settings. Explain face order, normals and closure.

## Slide 9
ALSO ISSUED
P1c — FIRST PRINT
DUE WEEK 8 — Oct 13 / 7%
The same geometry, made real. A printable variant of the project you have been building for two weeks — presented as a physical object at the midterm.
LIMIT
60 MM, 200 G
Each axis within 60 mm. The allocation includes failures.
RULE
NO SUPPORTS
Orientation is your only lever. Change the geometry if you must.
DUE
AT THE MIDTERM
The queue has latency the two-week cycle does not.

## Slide 10
REQUIREMENTS — P1c
Fabrication milestone — visual documentation 20% · computational understanding 20% · technical execution 15% · fabrication quality 30% · experimentation 5% · requirements 10%.
01
Develop a printable variant of the geometry project, within 60 mm on each axis and the 200 g allocation, with no supports.
02
Present the physical print at midterm with one orientation/process sheet and a photograph.
03
Submit the editable source, exported mesh and slicer project. Explain any geometry changes made for printability.
CHECKPOINT · WEEK 5 — Sep 22 — Review print-ready geometry, physical units, orientation and the sliced preview before queueing.

## Slide 11
NOW — BUILD THE PYRAMID
Rest of the session: from a single point to a closed solid that cuts.
✓
One point placed from an XYZ vector, and you can say why it is a position
✓
Four base corners and an apex, with Width / Depth / Height exposed
✓
All five faces joined — four sides and the base
✓
Closure checked: every edge shared by exactly two faces
✓
Cube minus pyramid working, off the same three inputs
LEAVE WITH A SOLID THAT CUTS. THE SHEET IS THE EASY PART.

## Slide 12
BEFORE NEXT CLASS
WATCH
U04 — Arrays and lists. Repeat Zone, Compare and Switch, and the nested grid. We start small and inspectable before anything scales up.
FINISH
P1a is due next class: the ordered diagram, the final axonometric and three variants.
BRING
Your pyramid, parametric and closed. Next week it becomes the component that gets repeated, so bring a file you can build on.
CHECK
Your FabLab orientation, before you need the machine rather than after.