## Slide 1
CLASS 09 / OCT 20 / U05
ATTRACTORS
P3 CONTINUES: THE RULE STOPS COMING FROM THE INDEX
MIDTERM UPLOAD CLOSED
P3c + P3study ISSUED TODAY

## Slide 2
AN ATTRACTOR IS A NUMBER
For every panel: how far is it from something? Use that number to drive a parameter.
THE WHOLE IDEA
for each panel p:
d = distance(p, a)
value = f(d)
Everything else this week
is a choice of f.
MEASURE IT FIRST
d = √((px − ax)² + (py − ay)²)
Pythagoras, once per panel. The answer is in model units.
Index told you where in the sequence. Distance tells you how far from something outside the collection.
IN ARRAYS YOU BUILT THE POSITIONS. NOW YOU MEASURE THEM.

## Slide 3
READ THE FIELD BEFORE YOU CHANGE ANYTHING
Distance is a value at every location. Look at it as grey before it becomes geometry.
01 MEASURE
Every location on the facade grid gets a number: how far to the attractor.
02 DISPLAY
Show those numbers as grey. This is a diagram already.
03 REMAP
Push that range into the range your parameter needs.
04 DRIVE
Only now does the panel change. The field was finished first.
THE FIELD, READ AS A GREY VALUE ACROSS THE FACADE · NEAR → FAR
IF THE GREY IMAGE IS NOT ALREADY A GOOD DIAGRAM, THE PANEL WILL NOT SAVE IT.
3.4 shows the attractors and the resulting variation side by side, with the parameter labelled. That order is the assignment.

## Slide 4
REMAP, AND SAY WHERE YOU CLAMPED
Distance comes out in model units. Your parameter needs a specific range.
THE OPERATION
t = (d − dmin) / (dmax − dmin)
t = clamp(t, 0, 1)
out = outmin + t × (outmax − outmin)
d 0 … 4 units ← input
out 0.85 … 0.15 opening ← output
SUBTRACT. DIVIDE. MULTIPLY. ADD.
Nothing here is new. It is the arithmetic of a transformation, applied to a distance instead of a coordinate.
Clamping is a decision, not a safety net. Decide what happens past the end of your range and say so. Swap the two output values and the pattern inverts.
3.4 LABELS THE PARAMETER AND SAYS, IN PLAIN WORDS, HOW DISTANCE CHANGES IT.

## Slide 5
FALLOFF, AND WHAT YOU MEASURE TO
f shapes the result. The attractor type changes only what the distance is measured to.
LINEAR
v = 1 − t
INVERSE
v = 1 / (1 + k·t)
SMOOTH
eased at both ends
STEP
on / off at a cut
ONE POINT
d = distance(p, a)
NEAREST OF SEVERAL
d = min(distance(p, ai))
NEAREST ON A CURVE
d = distance(p, closest(c, p))
SAME FACADE, SAME PANEL, SAME PARAMETER, THREE ATTRACTORS: 3.4 SHOWS WHAT THE ATTRACTOR ALONE CHANGES.

## Slide 6
THE SAME THING, WRITTEN OUT
Measure, remap, clamp, shape the falloff, then drive one parameter. In that order.
# Pseudocode: choose ONE of the three distance methods.
for p in panel_locations:
d = distance(p, point_a) # one point
# d = min(distance(p, point_a), distance(p, point_b))
# d = distance(p, closest_point(curve, p))
opening = remap_clamped(d, from_range=(0, 4),
to_range=(0.85, 0.15))
panel = build_panel(opening=opening) # same prefab, new input
place(panel, p)
WHAT IT MAPS ONTO
distance
external condition
field
remap
clamp
falloff
nearest
LINE 2 IS THE ONLY LINE THAT CHANGES BETWEEN THE THREE ATTRACTOR TYPES.

## Slide 7
THE NUMBER DRIVES YOUR 3.1 PANEL
Not a sphere, not a cube. The panel you already built, rebuilt at every location with a different input.
01 MEASURE
Distance from each facade location to the attractor. Object Info, set to Relative, so the attractor and the facade share one coordinate system.
02 REMAP
One Map Range, Float, Linear, Clamp on. Input 0 to the reach of the attractor. Output: the safe range of your parameter, in its own units.
03 DRIVE
Instance on Points repeats a thing that is already built. To rebuild the panel per location with its own Opening, Depth or Height, the value goes into a For Each Element zone and reaches the panel's input inside it.
IF ALL PANELS LOOK THE SAME: THE VALUE ENTERED THE ZONE OUTSIDE, BUT NEVER REACHED THE INPUT INSIDE.
Attractors.blend, scenes 05 to 08: the supplied panel, then one point, several points and a curve driving its Opening.

## Slide 8
ISSUED TODAY
P3study — ATTRACTORS - THREE FIELD STUDIES
DUE WEEK 10 — Oct 27
One facade, one panel, one controlled parameter, three attractors. Each diagram shows the attractor and the variation it produces, with the parameter labelled. No separate upload and no separate grade: it is page 1 of the 3.5 package.
DIAGRAM 1
ONE POINT
Distance to a single point drives the parameter.
DIAGRAM 2
SEVERAL POINTS
Say how they combine: nearest point, or an average.
DIAGRAM 3
ONE CURVE
Distance to the nearest location along a curve.

## Slide 9
ISSUED TODAY
P3c — ARCHITECTURAL APPLICATION
DUE WEEK 10 — Oct 27 / 10%
Reuse your 3.1 panel to design a simple facade, wall, canopy, pavilion or similar. Give it a purpose and a scale, choose the attractor that serves that purpose, and show why the variation matters architecturally.
PURPOSE
WHAT IT DOES
What the panel system encloses, screens, shades or defines.
COMPARE
ONE CONTROLLED TEST
The attractor, the parameter it drives, and the difference it makes.
RESOLVE
ELEVATION + ISOMETRIC
Two sheets with 3.4: studies first, then the application.

## Slide 10
REQUIREMENTS — P3c
Visual quality 35% · computational understanding 25% · technical execution 20% · experimentation 10% · requirements and identity 10%.
01
Reuse the panel you developed in 3.1 to design a simple facade, wall, canopy, pavilion or similar architectural application. You may develop your 3.2 architectural study further.
02
Give the design a clear purpose and scale. Explain what the panel system encloses, screens, shades or defines, and how attractor-driven variation supports that purpose.
03
Choose point, multiple-point or curve attractors. You do not need to combine every attractor type in the final design.
04
Show one controlled comparison and a resolved elevation and isometric. Identify the attractor, the geometric parameter it drives and why the variation matters architecturally.
05
A new precedent study is not required. Facadepot and other references may provide optional inspiration; credit any images or ideas you use.

## Slide 11
NOW — YOUR FIRST FIELD
Rest of the class: measure, look, remap, and only then attach your panel.
✓
Distance to one point, measured across the facade grid you already have
✓
The field shown as grey on its own, before any panel changes
✓
Input and output ranges written down, in your parameter's units, with the clamp
✓
One parameter of your 3.1 panel driven: Opening, Depth, Height or similar. Just one
✓
The attractor moved, and the change predicted before you look
MOVE THE ATTRACTOR. IF YOU CANNOT PREDICT WHAT HAPPENS, STOP AND READ THE FIELD.

## Slide 12
BEFORE NEXT CLASS
NEXT
Week 10 — Oct 27: 3.4 and 3.5 are submitted together at the start of class. Then 4.1 is introduced: the supplied field groups and a two-parameter matrix.
3.4
All three attractor types running on the same facade, same panel, same parameter. The comparison is what is being graded.
3.5
Pick the purpose first, then the attractor that serves it. One controlled comparison, one elevation, one isometric.
PANEL
Your 3.1 panel as a node group with the driven parameter exposed. Test two values by hand before you connect an attractor.